## Slide 1: PySAR Training Workshop
Zhang Yunjun
Geodesy Lab, University of Miami, FL
Nov 17th, 2017

## Slide 2: What’s PySAR?
PySAR is a open-source Python package for InSAR (Interferometric Synthetic Aperture Radar) time series analysis.
It reads stack of coregistered, unwrapped interferograms processed by ROI_PAC, Gamma or ISCE, and produces three dimensional (2D in space and 1D in time) ground displacement.
Download: git clone https://github.com/yunjunz/PySAR.git
Installation: https://github.com/yunjunz/PySAR#1-installation
Google Group: https://groups.google.com/forum/#!forum/py-sar

## Slide 3: How to use it?
Generate a template file: cd ~/KujuAlosAT422F650/PYSAR pysarApp.py -g
Modify ”Step 1. Load Data” options in pysarApp_template.txt to add the path of input files pysar.insarProcessor = roipac pysar.unwrapFiles = ~/KujuAlosAT422F650/ROIPAC/RADAR/filt_*.unw pysar.corFiles = ~/KujuAlosAT422F650/ROIPAC/RADAR/filt_*.cor pysar.lookupFile = ~/KujuAlosAT422F650/ROIPAC/RADAR/geomap*.trans pysar.dem.radarCoord = ~/KujuAlosAT422F650/ROIPAC/RADAR/radar*.hgt pysar.dem.geoCoord = ~/KujuAlosAT422F650/ROIPAC/RADAR/*.dem
Run pysarApp.py and check results plot in PIC folder! pyarApp.py
Test data KujuAlosA:

## Slide 4: Plot result using view.py and tsviewer.py, with -h for help/usage.
Mean LOS Velocity
Displacement History @ Kuju Volcano

## Slide 5: pysarApp.py Workflow

## Slide 6: pysarApp.py - steps
Load Data
  Subset (optional)
  Prepare geometry
Reference in Space
Unwrap Error Correction (optional)
Modify Network (optional)
Network Inversion

## Slide 7: pysarApp.py - steps (cont.)
Local Oscillator Drift Correction (for Envisat)
Tropospheric Delay Correction
Topographic Phase Residual Correction
  Phase residual RMS
Reference in Time
Phase Ramp Removal
Velocity Estimation
Post-processing: geocode, export, plot

## Slide 8: pysarApp_template.txt – basic rules
pysarApp.py runs in the order of options listed here in the file
To adjust your processing result, change the corresponding option value in the template txt file and re-run pysarApp.py
“auto” for default option value, with explanation in the comment in the same line
custom value input format/range is explained in the comment in the same line

## Slide 18: Play with plotting scripts – view.py
view.py geo_velocity.h5 --mask geo_maskTempCoh.h5 -u cm -m -2.5 -M 0.5 -c jet_r --lalo-label -d demGeo.h5
Feature Highlights
  DEM shaded relief background
  Lat/lon label; scale bar
  All colormaps from matplotlib
  --save/--nodisplay to save w/n display
  Custom figure/font size, output DPI
  Display with different refence pixel/date on the fly
  Check the current pixel coordinate / value on the status bar

## Slide 19: Play with plotting scripts – tsviewer.py
tsviewer.py geo_timeseries_ECMWF_demErr_refDate_plane.h5 --mask geo_maskTempCoh.h5
Click on the left panel to plot its displacement history on the right
Drag “Time Slider” on the bottom of left panel to see the animation!
--save / --nodisplay to save the plot data on text file
Feature
Highlights:

## Slide 20: Play with plotting scripts – plot_pysarApp.sh
Check the default plotting results in PYSAR/PIC folder.
plot_pysarApp.sh calls view.py to plot most of h5 file generated by pysarApp.py; change the plot setting within the file to adjust and save your plots in the style you like!

## Slide 21: Re-run pysarApp.py
After initial running and checking your results, you may want to adjust some parameters and re-run to update your result, PySAR makes it very easy.
Change the option value in pysarApp_template.txt, then run pysarApp.py directly. You don’t need to delete nor remove files, and pysarApp.py will start from the changed step and continue.

## Slide 22: What in PySAR but not in pysarApp.py
PySAR is a toolbox. There are a lot of other scripts besides pysarApp.py. Check them in $PYSAR_HOME/pysar director. All scripts can be ran individually, except for scripts starts with _, e.g. _readfile.py.
You can build you own processing recipe with it, check the example in $PYSAR_HOME/shellscripts
You can import pysar as a python module below and develop your own program based on it, check the jupyter notebook example in $PYSAR_HOME/examples: import pysar
Check API Document for complete list of scripts and modules/functions

## Slide 23: Have fun to play the InSAR time series!